PCB Irradiation Test - Next Analysis Steps
        Roman Pöschl
        LAL Orsay
        Calice Ecal Meeting
        6/2/08

---
Introduction
Calorimeter Electronics to be interleaved with layer structure
Do high energetic showers create signals directly in electronics ?
If yes, Rate of faked signals ?

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup I
Test PCB
- equipped with
  PHY3 Chip Set
Prepared Slab
- W dummy
- capton and paper
  for electrical shielding
Usual Slab
Picture courtesy of B.Lutz

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup II
- PCB positioned at place of layer 12 in Ecal ~ shower maximum
  x,y position identical to layer 2
- Schematic view of test PCB - 'Expect' signals from 72 pads, 4x18 = 2 Wafer
Nominal
positions
of
Chips
Scanning
points
Sketch by M.Reinhard/F.Salvatore
- 7 106 Triggers with 90 GeV Electrons (- 1 106 with 70 GeV Electrons)
  At least 250 K at each scanning point
  Runs 331462 – 331518
  Today: Analysis of 10k Events per analysed run
- Runs were subject to the same data processing chain as 'usual' runs

---
First Steps of Data Analysis – Rough Alignment Studies
Beam Impact at nominal center of Chip 1 (-8.33,0) cm
Projection of
Center of Chip1
onto layer 2
Looks like we've shot a bit too high and too close to the Ecal Border

---
First Steps of Data Analysis – Rough Alignment Studies
70 GeV e- - Beam Impact at nominal center of Chip 1 (-8.33,0) cm
Ghost Hit?
16 Hits
Layer 12
Projection of
Center of Chip1
onto layer 14
- Chip 1 well 'touched' by shower maximum
- Small Activity in Layer 12

---
Basic Spectra
Cut: Etot > 1000 Mips
valid for Energy dep.
and hit map(s) in layer 12
Missing layers clearly visible
Nhit/0.4Mip
Layer 12 only !
No signal beyond 1 MIP!!!

---
First Steps of Data Analysis – Rough Alignment Studies
Moving towards Center of Ecal (-7.8,0) cm
Projection of
Center of Chip1
onto layer 2
Change in impact position clearly visible
'Beam Spot too far left and too high ? - More detailed study needed !

---
First Steps of Data Analysis – Rough Alignment Studies
90 GeV e- - Moving towards Center of Ecal (-7.8,0) cm
27 Hits
Projection of
Center of Chip1
onto layer 2
- Chip 1 well 'touched' by shower core
- Small Activity in Layer 12 (bit larger than for 70 GeV and 'nominal' Center)

---
Basic Spectra
Missing layers clearly visible
Nhit/0.4Mip
Layer 12 only !
        No signal beyond 1 MIP!!!
70 GeV -> 90 GeV Layer 12 outside of shower maximum

---
   So far all runs have been reconstruction using usual reco software
        Now
        Discarding all (Offline) Pedestal Corrections

---
Typical Noise Distribution - “Signal Events” (Run331498 -6.3cm,6.2cm )

---
Typical Noise Distribution - “Pedestal” Events (Run331498 -6.3cm,6.2cm )

---
Scan over Chip 1

---
Scan over Chip 2

---
Scan over Chip 4

---
More slides and conclusions for next monday's
        analysis meeting ....