Overview on May Running Period
        Roman Pöschl
        LAL Orsay
        CALICE Ecal Meeting
        3/6/08
- Installation Period
- Beamline at FNAL
- Overview on Data taken
- Outlook on July Running

---
MTBF – Meson Testbeam Facility at Fermilab
We are here!!!
- Beam is created by a primary Proton beam of 120 GeV/c

---
Picture courtesy of V. Zutshi

---
CALICE Testbeam at FNAL
- Installation Phase: 7/4/08 – 25/4/08
- Commissioning Phase: 28/4/08 – 7/5/08
- “Physics Runs” Phase: 7/5/08 - 27/5/08
General Running Conditions:
- Day operation – Beam between ~6m and 6pm
- Testbeam delivery interrupted by “Shot Setup”
  for TEVATRON experiments ~2 hours during our running
- No major machine downtime
  Some failures towards the end of the running
  Compensated by two extra half days on 26/5/08 and
  27/5/08 – Running 6am – 12pm
  Agreement on short notice
FERMILAB provides excellent support for our running
 - see above
 - e.g. Extensive help during (non trivial) setup of computing

---
Installation at FNAL – The Start
G. Mavromanolakis AEM Talk
Everything arrived on time and UNDAMAGED at FNAL

---
Detector Installation
- Equipment ready by 25th of April – Ready to accept beam on the 29th of April
- Setup – Combined effort of DESY, Uni Heidelberg, NIU, LLR, LAL and FNAL
- Setup comprises SiW Ecal, Ahcal and TCMT
  plus beamline equipment

---
Sketch of the beamline
A.Kaplan, H.Li

---
Experimental Control
- Live demonstration (planned)
  Place yourself to
  http://calice-cam01.fnal.gov:8080
  http://calice-cam03.fnal.gov:8080
- Conferencing system
  - Daily operations meeting
  - Regular communication between calice control
    room at FNAL and 2nd Control room at DESY or
    colleagues elsewhere in the world
- Portal service (live demonstration planned)
  https://calice-portal01(2).fnal.gov
CALICE has implemented a first GDN foreseen for
future ILC (and beyond) experimentation
Main responsible Sven Karstensen (DESY)

---
Beam Bursts
Frequency Modulation of 345Hz
in Event Distribution
- DAQ Deadtime ~0.5msec
- DAQ Buffer Limit 2000 Events
- Bursts reduce efficiency of Data Taking
P.Dauncey, A.Kaplan

---
Results from G4Beamline Simulation of MTest
The FNAL Beam
Results from G4Beamline Simulation of MTest
Energy	Lead (mm)	#pions	#electrons	Ratio
1 GeV	0	710	9990 0.07
   0.5	15	129 0.12
     1	8	43	0.19
     2	5	6 0.83
     5	2	5	0.4
2 GeV	0	2440	9990 0.24
   0.5	200	486 0.41
     1	88	158	0.56
     2	46	27 1.71
     5	10 1 10
4 GeV	0	5030	9990 0.5
   0.5 1198 1585 0.75
     1	671	548 1.2
     2	308	110	2.8
     5	109	2 55
E. Ramberg, T.Rinn
Low rates at low particle energies

---
New Differential Cerenkov counter
New Differential Cerenkov counter
20m Upstream of Calice Detectors
Win Baker* copied design used succesfully in MIPP
Jim Kilmer in charge of construction
Counter commissioned just before CALICE arrival
Timing of signals is just fast enough to be included in CALICE trigger
“Inner PMT” - accepts light near threshold
“Outer PMT” - accepts light from plateau region
“Inner x OutBar” - highly specific as to particle species
* Best Wishes!
Outer PMT
Inner
PMT
     Inclusion of Cerenkov Counter
in Trigger to create “pure” (pion) samples
E. Ramberg

---
Cerenkov Pressure Curve
Electrons
Pions
B.Lutz
Increasing refraction index of Cerenkov Gas
Regular recording of Cerenkov Pressure Curve
Cerenkov Pressure in Calice Data Stream

---
   Timing of the Cerenkov Trigger
        E.Garutti, B.Lutz, A.Kaplan, V. Zutshi
Due to finite propagation time Trigger Signal from Cerenkov arrives
~60 ns (~10 DAQ clock ticks) after the '10x10 coincidence' –
        Trigger 'working horse'
- 10x10 Trigger signal has to be delayed
Example of Coincidences between:
10x10A, 10x10B
Cerenkov
100x100B (Muon Trigger)
Trigger Mix lead to “pure” pion
sample at ~200 Events/Spill
Partially large muon contamination
- Particles propagate faster than Cerenkov Signal
- Trigger Latency and details of signal formation in Calice Front Electronics
Þ Risk to record detector signal in falling slope (Discussed by Hengne and Marcel

---
“Luminosity” - Recorded Data
Mixed beam at
“high energies”
5-60 GeV
Constant Slope
indicates regular stable
data taking
“Pure” Pion beam
< 5 GeV
- Data sets with translated (5 points with 3cm horizontal distance)
  and rotated 10o and 30o
  Detectors
  Rotation worked fine apart from a few hickups (“Kinderkrankheiten”)

---
Calice Shift Plan May 2008
Remote
Shifts
from DESY
E.Garutti
Broad Participation in Shifts – (Once more) a great pleasure
       Apologizes to those not appearing in the screen shot

---
Summary and Conclusions
- First Successful New Steps in the New World
Citation E.Ramberg: “You showed me things about the beam I wasn't aware of”
“You guys can be poud of your experiment”
“You brought in the equipment I was waiting for”
Dear Erik and George et al,
Thanks for giving presentations on the Testbeam infrastructure and
the CALICE results.
They looked great! And I would like to congratulate and
thank every one of you who was involved in this effort.
All the very best,
Young-Kee
- Steep learning curve on how to take data and work in Fermilab environment
Strong support by Fermilab
- Commissioning of experimental setup parallel to data taking
Handling of Cerenkov Counter
Trigger Latency
Improvements by fast HERA-B PMT (Idea of Beni)
- Still already lots of interesting data on tape
- Let's draw the right conclusions for the July Running
9/7/08 – 29/7/08 (or longer)