Toward a DAQ for the DHCAL m³
(in Test Beams)
Vincent Boudry
LLR, École polytechnique
EUDET/Elec meeting
LAL, Orsay
02/06/2008

---
Time line
Cosmic DAQ
  - Running (new: analogue readout)
Summer Test beam DAQ:
  - PS: July 10-17→ adapted cosmic DAQ ?
  - SPS: Aug. 6-11 → Adapted CALICE DAQ0
  - PS: beg. Nov → USB DAQ (m²)
DAQ2 m³
  - summer 2009

---
Cosmic DAQ
Based on LabView (R. Della Negra)
  - USB readout & control of ≤5 cards (on HUB)
    Using libDHCAL (C. Jauffret)
  - Analogue RO of 1 card (Being tested)
Goal:
Characterise the Chamber, ASIC's, PCB's on cosmics
Calibrate the ASIC's (EC)

---
DHCAL1 board
8×32 pads detector (GRPC and µMEGAS)
  - 8-layer PCB
  - 4 HARDROC's (64 ch each)
integrated DIF
  - Code being re-used for the DHCAL DIF's
USB connector
  - libDHCAL developed
    → C driver, LabView interface

---
Analogue Readout Extension:
Goal: measure the shape of the signals
  - → optimisation of gains
Use of the VTC card of the ECAL cosmic bench
  - VTC = LLR DAQ for ECAL Cosmic bench
    - HW: Boards + cables
    - Readout 1 card
      - Eventuality 2 (with adapted cables)
Adaptation:
  - CPLD:	Number of channels (➘4) ,
    Number of cycles (➚64)
  - HW: LVDS signals DHCAL ≠ ECAL
  - HW: New analogue drivers (AD8138)

---
Cosmic DAQ: Analogue RO perf
First evaluation
  - Linarity,
Ex: Analog output of first ASIC1
  - dominated by coherent noise
OK for RPC response
Courbe de gain ASIC1
charge injectée (mV)
deltaV sortie ASIC (mV)
fC

---
Test beam DAQ in Aug.
5-6 DHCAL1 board (20 HR's) in PS & SPS beams
DAQ0 EUDET :
  - Use the complete DESY test bench
    - 1 CRC (⊃ 6 FE) + VME Crate & controller + PC (with DAQ soft)
  - Avail. Early July → mid. August
USB for control and digital readout
  - libDHCAL + Socket (being written [Simon Chollet])
  - Protocol already defined (last year!) with Paul Dauncey.
Config management & storing of data in LCIO files
RAW data Format to be defined
Analogue readout possible (level adaptation to be checked)
  - With analogue drivers replacement (done on 1 card now)

---
DAQ m² (TB @ PS November)
Direct USB readout of 3 DHCAL DIF.
  - 48 HardRoc/DIF, 144 in total
use the DHCAL DIF test bench DAQ
  - Based one XDAQ [see pres. Of Ch. Combaret]
  - Altern: CALICE DAQ0
Re-use of DHCAL USB code
  - Possible re-use of USB code for other DAQ's (ECAL Wafer, in-situ DAQ, ...)
Complementary with dev of next gen (DAQ2) ?
    - Database for the ASIC's configuration ?
    - Definition of the data format
    - Data classes
      - Should be compatible with LCIO format

---
DAQ2 overview for the m³
50/100 Mb/s
1 PC:	~2 k€
1 ODR:	~4-5 k€
1 LDA:	~1.3 k€
×4
Machine
clock
3(4) DIF × 40 planes / 10(8?) conn.
• no CC: 12 (15?) LDA + 4 ODR's
CC×8:	➔ 2 LDA, 1 ODR [5+4k€] + 12–20 CC
Total data volume: (All HR full)~40×144×20kb = 117Mb
➔ ~ 50 ms on 2 GigE, ×2 sur LDA-CC, ... DIF
5 ASICs / plane (max 18) × 128 bits × ~100Hz → 128 kB/s
DIFs
ASUs
DAQ2 PC
CC
Clock
& Control
Digital (Config, Controle)
Clock & Sync
LDA
ODR
LDA
CC
×10
⋮×8
Optique GigE
USB
×40
:
×12-20
:

---
Concentrator Card
Needed for DHCAL: 120 (40×3) DIF's
Goal
Characteristics
  - ×8 channels
  - USB readout
  - Cheap
Custom board
  - Cheaper (typ: 400€/card)
  - Prototype for a custom LDA:
    - → 40 channels
    - adapted for ILD embedding (see Rémi's talk)
Conceptual work started [Frank Gastaldi, Antoine Mathieu]
~Idem LDA
Transparent
Broadcast of configs to all DIF's
Avoid management of adresses
⇒ Modif of LDA's mecanism (ranges in place of fix adress), needed for redundancy ?
(DIF bypass ?)
VHDL Blocks common to DIF /LDA

---
Tentative Path & Planning for CC
Tentative agenda
Prototype 0 : Study of Firmware	≤ dec 08
  - Mezzanine card around a big FPGA (XILINX evalution card) → Sept 08
  - Connection on 4 DIFS.
  - USB readout
  - Test of communication protocols
Prototype 1: study for the production
8 DIFs
Merging of data
USB readout
scheme: sept–dec 08
Prod:	Jan-feb 09
Test:	Feb-Apr 09
Prep final prod:	Avr.-May 09
Production & test of ~20 cards
June-July 09

---
Merging scheme on CC / LDA
Scheme from LDA (M. Kelly)
  - → data format
5 MHz
40/50 MHz
On OK
Read
DIF 'n'
DIF 'n' OK
# Conn. DIF's
End of transm.
Link status

---
RAW Data format
ODR/LDA protocols [wrapping] well defined
RAW data format (≃”out of DIF”)
Allow for merging, with internal consistency markers
Example:
CC: Change the Nb_of_DIF, count data words & aggregate the data
Coding: 8b/10b corrects a bit the errors.
Allow for End of data signal
Inside a ”LDA block” (as proposed By M. Kelly): words of 16
Nb_of_DIF	(filled by DIF, modified on CC when merging)
n ×	| DIF_Header == Word Type + DIF_ID (typ. 8 bits) + type of Data (ASIC, SC, Config)
| Nb_of_ASIC	OR	| Nb_of_ADC_words	OR | Nb_of_SC_words
| n ×	| Nb_of_words (filled on CC/LDA ?)	| n × ADC data	|....
|	| ASIC Data stream
| DIF trailer (padding words)
+ K character send by the DIF
Move
Here ?

---
DAQ2 M³ Test Beam contingencies
ASIC's in auto trig
DHCAL Data rates in TB
  - Expected from 100 GeV π (J-C. Brient's note)
    - 5 ASIC's touched in average (max 18) / plane
    - All on the central DIF
  - 1 evt = 160bits
    - Readout time 1 ASIC @ 5Mb/s = 0.032ms
    - RO 1 plane ~ 0.16ms [6 kHz]
  - 1 full HR (128 events) = 20480 bits
    - Readout time 1 full HR @ 5Mb/s = 4ms
see Remi's talk for ECAL
TB rates: 104 (108 at FNAL ???) part/s during 10s/min (SPS mode).
RPC limitation: ~100Hz/cm²
µMegas: basically not limited...

---
DAQ2 TB working modes
Burst mode (≤128 FOR DHCAL)
No external trigger but independent recording of trigger mode (⊃ Timestamp)
(could be 1 HR recording Trigger bits)
Data sync internal [synchronisation on reset of BC ID on all HR].
Internal «RAM full» management needed
Every 128 DHCAL [16 ECAL] events
  - LOCAL: in DIF with immediate RO of SLAB
    - 4 ms for 100 GeV π's without Reset (avoid loss of sync)
    - Indiv DT: might be hard too handle.
    - Local storage of data ????
  - Global
    - fast Ramfull → DAQ (stop of Acq, RO of all chips, and restart)
    - periodic interruptions (counting of part ? Hodoscope HR ?)
Single Event
External trigger (hodoscope) → DIF
  - Stop Acq
  - Read chips:
    ~0.16ms (+ noise if any)
    ⇒ max 6kHz on 100 GeV π's
  - Start Acq
Data sync (for Event building)
  - On synchronized BC ID
  - On trigger timestamp (e.g. On DIF Timecounter on last internal trigger to ext. trigger)
Fine if not RAM full
e.g. # rejected triggers + noise event per chip < 128 [16 for the ECAL!]
  - Ideally: have a circular buffer

---
DAQ2 signals
DIFs
ASUs
DAQ2 PC
CC
Clock
& Control
Digital (Config, Controle)
Clock & Sync
LDA
ODR
LDA
CC
×10
⋮×8
Optique GigE
USB
×40
:
×12-20
:
×4
50/100 Mb/s
Machine
clock

---
Clock & Control Card [reminder]
AUTO / X-TAL
SW-0
A) CLOCK
LVDS on SMA
EXT.CLKIN
8x LVDS on HDMI
1
OR
LVTTL on Lemo
( 8x LVDS on SMA ? )‏
NIM on Lemo
MPX +PLL
2x LVTTL on Lemo
2x NIM on Lemo
~ 50 MHz
X-TAL
B) FAST TRIG
SW-1 2->1
LVDS on SMA
8x LVDS on HDMI
C) CONTROLS
( 1x LVDS TRIGGER on RJ-45 ? )‏
CPLD
4x LVDS on SMA
4x NIM on Lemo
SW-2 5->1
4x
4
4
8x LVDS on HDMI
D) BUSY
LVDS on SMA
1
1
SW-3 2->1
8x LVDS on HDMI
NIM on Lemo
OR
8
4
o/c TTL on Lemo
8
1
1
PCB-1 HEADER / CONNECTOR
MP + MW, UCL, 29-10-2007

---
DAQ2 planning: test & integration
Test Setup:
1 PC with DOOCS + libODR/device
1 ODR
1 LDA incl FW
1 CCC
1(2?) DIF
Test set-up in September ?
  - Test of HW (⊃ CC)
  - Protocols, data format, config loading
  - Acquisitions modes
  - Integration
    - Event display, slow control, config database

---
Conclusion
Lot of work ahead
Pending questions
  - Configuration distribution: PROM vs SWITCHES (Physical mapping)
    optimal topology (for redundancy)
  - Running modes
  - Trigger distribution
  - Minimal amount of RAM in DIF, CC, and LDA.
  - Complete out of DIF Data format
Need some clarification on many points to have a working set-up for next year
  - Meeting tomorrow 9am room 032