HAPS Controls
Glen White
ATF2 Software Review Workshop, LAL, June 2008

---
Layout of Controls

---
Controls Summary
Software written to control and monitor Bulk Power Supplies and EPSC controllers.
Bulk PS's controlled through Allen-Bradley PLC interface
  - Using configured EPICS driver and database from R. Wright, K. Kasemir (SNS) over tcp/ip to PLC (ETHER_IP EPICS module).
Control and monitoring of redundant HAPS modules through EPSC using purpose-written EPICS driver, database and Matlab/LabCA-based panels.
  - Driver built using ASYN driver framework interacting to EPSC hardware over tcp/ip.
All controlled from single 'soft' EPICS IOC installed on a standard PC running linux.

---
HAPS Controls at ATF2
ATF-LOCAL Subnet (EPICS)
Linux PC Running EPICS IOC
(2 ethernet cards )
PS Local Subnet
PLC
Bulk
PS
Bulk
PS
Bulk
PS
Bulk
PS
Bulk
PS
Bulk
PS
6 Bulk Power Supplies
HAPS
HAPS
HAPS
HAPS
HAPS
... (38 PS's)

---
Main Panel

---
EPSC/Bulk PS Panel

---
Expert Panel

---
Power Modules Panel

---
Documentation
Documentation on SLAC wiki
https://confluence.slac.stanford.edu/display/ATF/ATF2+Magnet+Power+Supplies
List of PV's available and use instructions
Instructions for test GUI panels
Configuration data
Hardware info
Expert documentation (EPSC server info, PLC documentation etc)
Software CVS repository info and installation instructions

---
Simulation Mode
EPICS PV's that normally communicate with PLC's and EPSC devices have SIML fields which change their behaviour if SIM_MODE record VAL set to 1.
Code in main driver causes current readbacks to mirror IDES values.
Alarm status fields behave as in production mode.