Sebastian Weber
University of Wuppertal
Integrated LED calibration

---
University of Wuppertal & ILC
Join ILC and proceed developement of „integrated LED“ calibration system
start with existing test
system
optimize
  - circuit
  - LED position & color
develop robust, scalable
& simple calibration
sytem

---
Plans
xy table
  - high resolution homogenity test
  - LED position
  - β-rays
  - edge of tiles?
highly automated system
  - scan through a set of parameters in short time

---
Plans
Temperature controlled box
  - reproducibility
    - actual system highly sensitive to temperature
  - temperature studies

---
DAQ
HCAL DAQ (VME+CRC) less convenient
  - CRC rare
  - complex
  - expensive
  - overkill (e.g. >1700 SiPMs)
Our Requirements
  - small, easy to use and adaptable hard- and software
  - read out ~4 SiPMs
  - still as similar as possible to existing system

---
µDAQ
A lightweight DAQ system on 100x80mm²

---
µDAQ Features
Full support of HCAL LVDS signals
  - 68 pin VHD SCSI connector
Analog part 1:1 identical with CRC
  - 4channel ADC: up to 72 SiPMs
Generates all supply voltages except HV
USB interface
  - RS232 emulation
  - Drivers for all OS → no pain for developers
Up to 3 Temperatures
Hardware developement completed
  - software no show stopper

---
µDAQ Features - timing
CRC
  - HOLD signal: 200-1000ns, 6.5ns steps
  - 52ns LED pulse by 300MHz pulse generator
    - (fixed delay to HOLD)
µDAQ
  - only 83ns steps
  - keep HOLD fixed
  - shift LED pulse delay instead (300MHz generator)
What's about jitter on µCs?
  - Measured to be less than 140ps

---
Outline
Integrated LED calibration system taken over by University of Wuppertal
µDAQ hardware completed
software less critical
We can begin within next weeks!