Analysis of PCB Irradiation Tests
        Roman Pöschl
        LAL Orsay
- Motivation
- Experimental Setup
- Data Samples
- Analysis and Results
- Summary, Conclusion and Outlook
Calice Collaboration Meeting Daegu/Korea Feb. 2009

---
Introduction
Calorimeter Electronics to be interleaved with layer structure
Do high energetic showers create signals directly in electronics ?
If yes, Rate of faked signals ?

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup I
Test PCB
- equipped with
  PHY3 Chip Set
Prepared Slab
- W dummy
- capton and paper
  for electrical shielding
Usual Slab
Picture courtesy of B.Lutz

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup II
- PCB positioned at place of layer 12 in Ecal ~ shower maximum
  x,y position identical to layer 2
- Schematic view of test PCB - 'Expect' signals from 72 pads, 4x18 = 2 Wafer
Nominal
positions
of
Chips
Scanning
points
Sketch by M.Reinhard/F.Salvatore
- 2.6 106 Events with 90 GeV Electrons (- 5.8 105 with 70 GeV Electrons)
  At least 70 K at each scanning point (Details see later)
  Runs 331462 – 331518
  Today: Analysis of 10k Events per analysed run (nearly) Full Statistics
- First Step: Runs were subject to the same data processing chain as 'usual' runs

---
First Steps of Data Analysis – Alignment Studies
Beam Impact at nominal center of Chip 1 (-8.33,0) cm
Projection of
Center of Chip1
onto layer 2
Looks like we've shot a bit too high and too close to the Ecal Border

---
First Steps of Data Analysis – Rough Alignment Studies
70 GeV e- - Beam Impact at nominal center of Chip 1 (-8.33,0) cm
Ghost Hit?
16 Hits
Layer 12
Projection of
Center of Chip1
onto layer 14
- Chip 1 well 'touched' by shower maximum
- Small Activity in Layer 12

---
Basic Spectra (for 10k Events)
Cut: Etot > 1000 Mips
Missing layers clearly visible
Nhit/0.4Mip
Layer 12 only !
No signal beyond 1 MIP!!!

---
First Steps of Data Analysis – Rough Alignment Studies
Moving towards Center of Ecal (-7.8,0) cm
Projection of
Center of Chip1
onto layer 2
Change in impact position clearly visible

---
First Steps of Data Analysis – Alignment Studies
90 GeV e- - Moving towards Center of Ecal (-7.8,0) cm
27 Hits
Projection of
Center of Chip1
onto layer 2
- Chip 1 well 'touched' by shower core
- Small Activity in Layer 12 (bit larger than for 70 GeV and 'nominal' Center)

---
Basic Spectra (10k Events)
Missing layers clearly visible
Nhit/0.4Mip
Layer 12 only !
        No signal beyond 1 MIP!!!
   70 GeV -> 90 GeV Layer 12 outside of shower maximum

---
   So far all runs have been reconstruction using usual reco software
        Now
        Discarding all (Offline) Pedestal Corrections
- Methodology:
  Subdivision of Runs into BeamTrigger and
  Pedestal Trigger Events (Oscillator Trigger) interleaved
  with beam events
  Expectation no difference between spectra in the both cases

---
Statistics of Analysis
Scan 3
Scan 4
Run331495: e-?? GeV
Signal: 314275 Evts.
Pedestal: 15264 Evts.
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 38295 Evts.
Run331498: e- 90 GeV
Signal: 66655 Evts.
Pedestal: 4223 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331494: e- 90 GeV
Signal: 65249 Evts.
Pedestal: 3602 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331497: e- 90 GeV
Signal: 214418 Evts.
Pedestal: 13666 Evts.
Run331474: e- 90 GeV
Signal: 85884 Evts.
Pedestal: 4949 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Scan 1
Scan 2
Run331473: e- 70 GeV
Signal: 208885 Evts.
Pedestal: 38295 Evts.
Run331488: e- 90 GeV
Signal: 213369 Evts.
Pedestal: 13719 Evts.
Run331471: e- 70 GeV
Signal: 10879 Evts.
Pedestal: 1950 Evts.
Run331479: e- 90 GeV
Signal: 85543 Evts.
Pedestal: 4306 Evts.
Run331480: e- 90 GeV
Signal: 85188 Evts.
Pedestal: 4678 Evts.
Run331491: e- 90 GeV
Signal: 217711Evts.
Pedestal: 11053 Evts.
Run331472: e- 70 GeV
Signal: 189966 Evts.
Pedestal: 37137 Evts.
Run331478: 90 e- GeV
Signal: 65249 Evts.
Pedestal: 3602 Evts.
Run331492: e- 90 GeV
Signal: 89435Evts.
Pedestal: 4254 Evts.
Run331486: e- 90 GeV
Signal: 129778 Evts.
Pedestal: 6146 Evts.

---
On Run Selection and Observations
- Run Selected according to entries in the logbook
  No comments on bad quality by Shift Crew
- Switch of energy between Run 331473 and Run 331478
  - Change in Pedestal Rate
    20% of all events -> 5% of all events
    Still at least 3500 of (valuable) pedestal events
- at least 70 at each point
   - ... but Run 331471 poor statistics 10k (can be increased by using 331470)
     very first scanning point
   - mostly 90 kEvents for off center runs
   - > 200k at (nomincal) Chip Center

---
Noise Spectra Scan 1
Signal Events
Pedestal Events
Scan ID
C
h
I
p
ID

---
Noise Spectra Scan 2
Signal Events
Pedestal Events
Scan ID
C
h
I
p
ID

---
Discussion of Noise Spectra
Disclaimer will show only a selection of plots
  - Full set of scan plots in Annex to talk
- First Order: No difference between signal and pedestal events
  visible
- Signal looks slightly shifted w.r.t pure Pedestal events
  Larger tails
  Number of Hits above MIP threshold O(10-5)
- No obvious dependency on scan position
- Next step - Test “gaussianess” of a signal
Expectation: Pedestal events should lead to pure Gaussian
        noise distribution
Method: Determine χ2/ndf for different fit ranges
Fit Ranges: (-4,4), (-8,8), (-12,12), (-16,16) ADC Counts

---
“Gaussianness” in Scan 1
Signal/5 ADC Counts
Pedestal
χ2/ndf
5
5
5
5
|Fit Range|

---
“Gaussianness” in Scan 2
Signal/5 ADC Counts
Pedestal
χ2/ndf
5
5
5
5
|Fit Range|

---
“Gaussianness” in Scan 3
Signal/5 ADC Counts
Pedestal
χ2/ndf
5
5
5
5
|Fit Range|

---
“Gaussianness” in Scan 4
Signal/5 ADC Counts
Pedestal
χ2/ndf
5
5
5
5
|Fit Range|

---
Discussion of Gaussian Behaviour of Noise Spectra
- Clear tendency observed
  Noise spectra in Layer 12 much less gaussian in Signal Events
  than in Pedestal events
  Average χ2/ndf in Pedestal events ~3
  Remember χ2/ndf for Signal Events has been divided by 5
   But ... no dependency on scan position visible!!!
- Chips are obiously sensitive to activity in detector when energy
  is deposited
  Small Insulation problem?
- Next step: Quantify global changes between signal and
  pedestal events
  Back to mean and rms
  as gaussian is maybe not a meaningful quantity

---
Average Mean and RMS for Scan 1
Difference
normalized
to MIP
=>
Global
effect
1% of MIP
Difference
normalized
to MIP
=>
Global
effect
<0.5% of MIP
No dependency on scan position visible

---
Average Mean and RMS for Scan 2
Difference
normalized
to MIP
=>
Global
effect
1% of MIP
Difference
normalized
to MIP
=>
Global
effect
<0.5% of MIP
No dependency on scan position visible

---
Average Mean and RMS for Scan 3
Difference
normalized
to MIP
=>
Global
effect
1% of MIP
Difference
normalized
to MIP
=>
Global
effect
<0.5% of MIP
No dependency on scan position visible

---
Average Mean and RMS for Scan 4
Difference
normalized
to MIP
=>
Global
effect
1% of MIP
Difference
normalized
to MIP
=>
Global
effect
<0.5% of MIP
No dependency on scan position visible

---
Summary, Conclusion and Outlook
- Analysis of PCB Irradiation test extended to (nearly) full statistics
- #Events beyond 1 MIP appear at O(10-5)
No evidence that shower particles create fake hits in detector
- Energy deposit in detector distorts the gaussian noise spectrum
  - Small sensitivity to detector load, Floating currents etc.
  - Let usual noise very rarely fluctuate above MIP threshold (45 ADC Counts)
- Global effect of parisitic signals (whereever they come from)
  is O(1% of a MIP) on the average signal and not measurable
  in the width i.e. rms of the detector noise
  (Which is also good news for all other SiW Ecal Analyses)
- All observed effects seem to be independent of scan position
- Plan to report presented results as contributed paper to TIPP09
- Paper for NIM should be accompanied by a simulation study
  First ideas exchanged with Christoph

---
Annex: Noise Spectra

---
Scan 1

---
Scan 1

---
Scan 2

---
Scan 2

---
Scan 3

---
Scan 3

---
Scan 4

---
Scan 4