Status of the Data Concentrator Card
and the rest of the DAQ
Vincent Boudry
Franck Gastaldi
Antoine Matthieu
David Decotigny
DHCAL meeting
20 jan. 2009
LLR

---
EUDET DAQ2 for the DHCAL
Clk ~ 100 MHz
(N×MClk)
Machine
clock
(5 MHz)
DIFs
(×120)
ASUs
DAQ PC
DCC
Clock
& Control
LDA-DIF on HDMI (Config, Control, Clock, Data, Sync)
Clock & Sync on HDMI (compatible LDA-DIF)
LDA
ODR
LDA
DCC
×10
⋮×9
Optique GigE
Debug USB
×40
:
×14
:

---
The 1 m2 electronics (quick status)
Julie Prast & Guillaume Vouters
DIF
10-layer board (6 for signals) designed and prototype produced
FirmWare & SoftWare operationnal and tested in beam
(with 4 HR µMegas card)
USB
HDMI
ASUs
RPC: 50×33.3 cm² (24 HR) boards produced & tested
μMeGas 32×8 cm² 4 HR produced
and tested
HR1 ASICs used
μMeGas Test board
“RPC” ASU
μMeGas + 4 HR ASU + DIF TB data available
⇒ not yet analysed

---
EUDET DAQ2 for the DHCAL
Machine
clock
 DCC being developped at LLR
120 DIF → 12 LDA → 4 ODR
Gain for DCC ≤ 1600€
120 DIF → 14 DCC → 2 LDA → 1 ODR
DIFs (×120)
ASUs
DAQ2 PC
DCC
Clock
& Control
Digital (Config, Control, Data)
Clock & Sync
LDA
ODR
LDA
DCC
×10
⋮×9
Optique GigE
Debug USB
×40
:
×14
:

---
Carte DCC
Goals
Transparency on the path DIF-LDA
Optimization of flux
Low cost
- Pre-proto (proto-0)
  - 4 DIFs connections
  - Implantation et tests du code VHDL
- Based on a XILINX evaluation board:
  - 128 Mbits SDRAM
  - Daughter board:
    - HDMI connecteurs
    - USB blocs
Franck Gastaldi
Antoine Matthieu
- Développements:
  - Marc Kelly (U. Man) : blocs Ser-Des, coding 8b/10b
  - USB blocs (Clément Jauffret)
  - Original VHDL blocs:
    - Memory controller, commands, buffers (FIFO),…..)

---
Daughter board
DIF Side
LVDS Signals (TX & RX)
USB part
LDA Side
MEMORY

---
DCC prototype data flux
Modified from Matthias
DCC
Memory
FPGA
LDA
DIF (×9)

---
DCC Proto-1
VME 6U
VME 6U
16×1 MB ZBT
(no latency BUS RAM)
Spartan 3
(1500 K gate)
Cost est.:
- 5 protos: ~ 800€/card
- 20 prods: ~450€/card
(Components: ~230€/card)
FTDI
Est: 1.2A	10mA	400mA	2.25A	30mA

---
Planning DCC
- January 09:
  - Finalisation of Schematic
    and routing of PCB
    - equal length of lines
    - inversion of diff lines
January- April 09
  - Fabrication of prototype
  - Test bench mounting
  - Validation & integration of VHDL blocs
- Mai – June 09 (estimation)
  - Production of boards for the m³
Looping DCC-DIF / DCC-LDA
Connection with the DIF (code on DIF: started)

---
DAQ2 Hardware: status of 12/12/08
http://ilcagenda.linearcollider.org/conferenceDisplay.py?confId=3196
LDA:
Components:
  - 1 Proto-DIF ✔, ECAL DIF (5 protos) ✔
    - Integration code LDA-DIF on going
  - 1 LDA (HW ✔, FW ongoing)
  - 1 CCC ✔ (2 cards avail., 8 more in prod)
  - 1 ODR v2 + 1 PC DAQ ✔ (mid feb.)
  - 1 proto DCC (march) or proto-0
- HW and protocoles: on-going → March ?
- Mars 09 →Jun 09
  - DAQ code DOOCS
  - Integration for a m³
    - Config Database (calib)
    - Slow Control, Event Display
    - Raw online analysis
    - SLCIO data writing
CCC:
ODR + PC

---
DAQ2 FW components
DIFs Commands/Protocole:
- User Manual being written
  - See M. Reinecke presentation
  - fast commands
    - sync, start/stop ACQ, trigger, reset BCID
    - specific commands for CALOs and DCC
  - Slow commands and Data transfer
    - power, reset, modes (sleep/idle), power pulsing
- Data format → LDA ~fixed
- DIF code sharing can start...
- Addressing still needs clarification
- DIF code (Many)
  - integration of DIF-LDA module
- LDA code (M. Kelly)
  - Ethernet OK
  - DIF code OK
  - Middle part on-going

---
Command Interface - Structure
Prototyping
Debugging
Final
Setup
- DIF clock (from LDA): 100MHz (40-120MHz).
- Standard data transfer: 8b/10b channel-coding.
Trigger/RAMFull: uncoded.
USB interface emulates LDA interface (clock-source: free of choice).

---
DAQ2 SW components: DOOCS
User
Application layer
Communication
Middle layer
Hardware Interface Layer
Software Libs
Sun/Linux Cluster
Software development and code base
Computer Infrastructure

---
DAQ SW components: DOOCS
- Drivers: ODR √ vers 2 ongoing
  - Used to test an emulated LDA
  - LDA, DIF, DCC: not yet
  - CCC: just started with HW
- Prototype DB for cards
  (LDA, DCC, DIF, ASICs)
  parameters (Valeria Bartsch)
DOOCS DAQ running with ODR
no state machine yet

---
DAQ2 SW To do's & Timeline

---
DAQ2 test benchs
- Meeting 12/12/2008 in DESY: needs of various groups
- 1st bench in UK: being build
- 1 bench in LLR:
  - DAQ PC + ODRv2 mid-February
    - now: PC + DCC pre-proto
  - test with USB connection on DCC, Debug DIF → for cosmic test
    - scripting (python ?)
  - integration of all DOOCS components
    - LCIO data writing
    - Event display
    - Database integration with LCDB (MySQL based)
    - Slow Control
  REM: knowledge passing ASAP
D. Decotigny

---
Summary
- All HW component for the DAQ are now available
  - some need extra prod (LDA, CCC)
  - DCC is advancing well according to planning
    - test prod this month (3 wks)
- FW: on-going everywhere
  - DHCAL DIF OK for USB but needs integration of DIF-LDA blocks
  - Effort of DIF Task force to write modular code on-going
  - LDA & DCC in intensive development
  - Protocol definition crystallising
- SW: Almost full skeleton working
  - integration of HW started
  - needs implementation in a real test bench with real objects
    (in part. ASICs) → @ UCL and LLR soon
- Good hope for full working system at end of spring