Ideas for a Tungsten HCal Prototype
CALICE Collaboration Meeting, Lyon
September 18, 2009
Christian Grefe
CERN, Bonn University

---
Outline
Motivation
- Simulations show tungsten is a viable option as HCal material at CLIC
  - See talk by Angela Lucaci-Timoce
- Engineering solution is available
  - See talk by Ronan McGovern
- Next step: full tungsten HCal prototype

---
What to learn from the Prototype?
- Physics performance
  - Verify simulations (resolution, shower shapes, ...)
  - Include realistic noise levels (neutrons)
- Tungsten plate production process
  - Test production of large thin plates
  - Feasibility of needed flatness
  - Machining of tungsten plates
  - Bolting, cutouts
- Mechanical questions
  - Assembly in view of full HCal module
Use different materials – tungsten vs tungsten alloys (Inermet)

---
What to learn from the Prototype?
- Use existing CALICE active modules
  - Test all available technologies in combination with tungsten
- Fill empty volume with steel and use as veto → only use fully contained showers
- 12 mm tungsten plates (to be discussed)
- Use pure tungsten and tungsten-alloy plates (no impact on physics, mechanical studies)
Veto
Tungsten
Calorimeter
Beam

---
Longitudinal Size
- 95% contained energy → ~40 layers (~4.8 )
- More than 50% of the events are fully contained
95%
12 mm tungsten + 5 mm Scint + 2.5 G10

---
Lateral Size
- 95% contained energy → ~40 cm radius
- Only 20% of the events are fully contained
95%
12 mm tungsten + 5 mm Scint + 2.5 G10

---
Which Dimensions?
- Cut on shower size biases physics
  - Small shower → large electromagnetic fraction
  - Large shower → large hadronic fraction
- Lateral size more important than longitudinal size
  - Event selection by first interaction does not bias the physics
  - Easy to add layers later
- Cost !!!
- Tungsten weight:
  - 80 cm x 80 cm x 1.2 cm x 40 x 19 g/cm³ ≈ 5.8 t
  - 60 cm x 60 cm x 1.2 cm x 40 x 19 g/cm³ ≈ 3.3 t
- Really need to understand the shower composition → further simulation studies

---
Conclusion & Outlook
- Prototype is important step if we seriously want to investigate tungsten HCal option
- Reuse of existing active modules
  - Scintillator & MicroMegas & ...
- Possible size: 80x80x80 cm³
  - Need further studies to understand needed size
- Tungsten HCal prototype discussion – September 24, LAPP Annecy
  - http://indico.cern.ch/conferenceDisplay.py?confId=68025
- Schedule
  - 2010 – production of tungsten plates
  - 2011 - testbeam?

---
Backup Slides

---
Coil Parametrization
Coil Parametrization
Alain Hervé

---
Coil Parametrization
Alain Hervé

---
Coil Parametrization
Alain Hervé

---
Tungsten Properties
Tungsten Properties
Pure tungsten
  -  = 19.3 g/cm3
  - λ = 9.94 cm, X0 = 0.35 cm
  - brittle and hard to machine
Tungsten alloys with W > 90% + Cu / Ni / Fe
  -  = 17 – 19 g/cm3
  - λ ≈ 10 cm, X0 ≈ 0.4 cm
  - Well established production procedure
  - Easy to machine
  - Price ~ 70 Euro/kg (without machining)

---
Tungsten Production
Tungsten Production Process
- Starting from powder, the metal mixture is first pressed and then scintered and finally machined
- Each production step increases the density
- The main limitations are:
  - Plate size – limited by the size of the oven
  - Thin plates – it has to be somehow stable after pressing
  - todays limitations are around 10 x 500 x 800 mm3
We are in contact with industry to address these issues
www.plansee.at

---
Tungsten Alloys
Tungsten Alloys
- Tungsten is usually used in alloys for better mechanical properties and machinability
- Several ferromagnetic (W,Ni,Fe) or paramagnetic (W,Ni,Cu) alloys are available
www.plansee.at

---
Tungsten Alloys
www.plansee.at