Update on Test Beam Results Using an
RPC Semi-Digital HCAL
Khaled Belkadhi
LLR-École polytechnique
belkadhi@llr.in2p3.fr

---
Présentation
Outline
- Introduction
  - The sDHCAL prototype
    - Mini sDHCAL
    - 1 m² prototype
  - Beam Tests history.
- Mini sDHCAL:
  - Efficiency and Multiplicity.
  - Uniformity and Stability in time
- 1 m² performances
  - Data selection
  - Efficiency results
  - Tracking system
- Conclusion
Key characteristics
for the energy reconstruction
in a digital calorimeter

---
Introduction
Grid (Steel)
Absorber (2 cm)
ASIC (HARDROC1)
PCB
Pads (copper, 1 cm2)
0V
Insulation (Mylar)
Anode coating(~10 M/)
Glass plate (0.7mm)
-HV
Chamber wall (1.2mm)
    RPC and semi-digital calorimeter
Glass plate (1.1mm)
Cathode coating(~10 M/)
Gas
Spacer

---
Déroulement de la formation
Introduction
- SDHCAL prototype
  - Mini sDHCAL
    - RPC: 4 Asics and 8*32 of
      1 cm² cells
    - Asic: 64 Channels
    - Trigger = 2 scintillators
  - 1 M² :
    - 144 Asics
    - Same triggering
      system

---
Beam tests and
List Of Participants
2008	July/August / Mini sDHCAL / 3-12 GeV Pions PS@CERN	November / Mini sDHCAL / 6 GeV Pions PS@CERN
2009	June July / Mini sDHCAL + 1 M² / 3-12 GeV Pions PS@CERN	August / Mini sDHCAL + 1 M² with Absorber / 10-150 GeV Pions&Muons SPS@CERN
IPNL (France): C. Combaret, I. Laktineh, R. Kieffer, M. Vander Dockt
LLR (France): K. Belkadhi, V. Boudry, D. Decotigny, M. Ruan
CIMAP (Spain): M-C. Fouz, J. Puerta Pelayo
CP3 (Belgium): E. Cortina, S. Manai
FST (Tunisia): K. Manai

---
Formats des documents 1/2
Time reconstruction
Time structure:
Trigger
First event
Acquisition
Starts acquisition
Events are recorded in the memory
with corresponding time and
channel ID
Trigger from scintillators: stops
acquisition
Read the memory
Isolated hit
 (noise)
Asic N°
Hits in time
Trigger event
Time reconstruction
Hits belonging to the same event have |Dt|<200 ns: selection criteria for tracks reconstruction
Time
Time to trigger (ms)
Dt (ms)

---
Tracks Reconstruction
- Efficiency/Multiplicity determination:
  - Tracking method:
    - Use hits belonging to the
      remaining RPCs with a time
      selection to build a track
    - Serach hits in the studied
      layer around the expected
      impact
Double hit
Event Selection:
Dt<200 ns
≥1 hit per selection layer
DX & DY = ± 1 cm on all layers
Single hit
Layer1
Layer2
Layer3
Layer4

---
Formats des documents 2/2
Efficency and Multiplicity Vs HV
Reference setup: 4 Russian RPCs, Triggered event data sample
Number of cells in the RPC(>1)
HV scan
Threshold 220 DAQ value
6 GeV pions beam
Uniform behaviour for the 4 RPCs
95% of efficiency reached at 7.4 kV
Multiplicity of ~ 1.6 at 7.4 kV

---
Efficency Vs Threshold
SDHCALwith 1st version of Asics
= 2 thresholds
****Start of signal distribution
More to be seen with the 2nd version
 of Asics
→ Working thresholds choosed:
Low threshold 220 DAQ value
High threshold 450 DAQ value
HV = 7.4 kV

---
Formats d'enregistrements
Multiplicity distribution
Full Train Sample: reconstructed multiplicity
Multiplicity per layer
(thr = 220; HV=7.4kV)
Global Multiplicity

---
Detector Uniformity
Efficiency 2D map RUN 102, HV=7.4 kV
1
2
3
4
-Bulk uniformity dispersion <~3% (including statistical error)
Y
X

---
Systematical Effects
High rate areas (19 kHz/cm²)
Efficiency map RUN 179
Fish line between the two plates
Beam profile
Fish line will be replaced by ceramic balls
to reduce contact surface

---
Stability in time HV =7.4 kV

---
1 M² prototype

---
1 M² data Structure
Time selection for cosmic
related events:
0< EventTime<1.2 ms
Noise contamination ratio: 1%
Noise
Signal+Noise

---
Efficiency and Multiplicity results
Position scan
1	4	7
2	5	8
3	6	9
Results without gain correction
and at different T,P,H (to be controlled in next beam tests)

---
Tracking System
Small set-up (mini-DHCAL) used as tracking device for the large chamber

---
Tracking System
Offline reconstruction:
Clustering in small chambers
Fit track in small chambers
Project track in Large chamber
Check hit presence.
Small Setup
100x100 cm2
Large Chamber
Distance between expected and found hits
Good synchronisation and alignment between
the two detectors

---
Conclusion
- Study of efficiency and multiplicity of the detector confirms the high performances with the optimal parameters:
  - Efficiency ~ 95%
  - Multiplicity ~ 1.5
- Study of stability and uniformity of the detector.
- 1 M² RPC: everything is working now (efficiency >94%).
- Next:
  - Two additional large RPCs being assembled
  - Two scheduled beam tests:
    - May: 2 weeks PS beam
    - July: 11 days SPS beam