     Hadrons in a SiW Electromagnetic Calorimeter for a
        Future Linear Collider
LHC
       Roman Pöschl
        LAL Orsay
        EUDET Annual Meeting DESY Hamburg
        September/October 2009

---
Hadronic Decays of W and Z Bosons
Boson Boson Scattering
    What if no Higgs?
W, Z separation in the ILD Concept
     Manifestation of new physics
Strong Electroweak Symmetry Breaking
Jet
Jet
Jet
Jet
Remember: MZ-mW ≈ 10 GeV
- Need excellent jet energy resolution to separate W and Z bosons
  in their hadronic decays
  3%/Ejet-4%/Ejet
- Basic mean: Highly granular Calorimeters

---
        SiW Ecal - Basics
Basic Requirements
The SiW Ecal in the ILD Detector
- Extreme high granularity
- Compact and hermetic
Basic Choices
- Tungsten as absorber material
   - X0=3.5mm, RM=9mm, I=96mm
   - Narrow showers
   - Assures compact design
- Silicon as active material
  - Support compact design
  - Allows for pixelisation
  - Large signal/noise ratio
SiW Ecal designed as Particle Flow Calorimeter

---
SiW Ecal Optimisation
        LOI for 2009 ILC Detectors
Optimisation using Jet Events and Pandora Particle Flow Algorithm
        (see talk by M. Thomson)
Lateral granularity of SiW Ecal
Jet Energy resolution strongly sensitive
on cell dimensions
- Better separation power
- Importance grows towards higher
  energies
High granularity of Ecal is crucial for precision measurements

---
The Calice Mission
Final goal:
A highly granular calorimeter optimised for the Particle Flow measurement of multi-jets final state at the International Linear Collider
Intermediate task:
Build prototype calorimeters to
Establish the technology
Collect hadronic showers data with unprecedented granularity to
- tune clustering algorithms
- validate existing MC models
E. Garutti
Si-W ECAL
Scint. Tiles-Fe AHCAL
Scint. Strips-Fe TCMT
Imaging
calorimeter

---
SiW Ecal Physics Prototype
30 layers of Tungsten:
• 10 x 1.4 mm (0.4 X0)‏
• 10 x 2.8 mm (0.8 X0)‏
• 10 x 4.2 mm (1.2 X0)‏
‣ 24 X0 total, 1 λl
½ integrated in detector housing
⇒ Compact and self-supporting detector design
        6x6 PIN Diode Matrix
   Resistivity: 5kcm - 80 (e/hole pairs)/µm
Shielding
PCB
Tungsten: H structure
Thickness:
 525µm
Front End
electronics zone
62 mm
Total: 9720 Pixels/Channels
Silicon wafer
62 mm

---
Large Scale Beam Tests
     Experimental Setup
Particle Distance~ 5 cm
 No Confusion !!!
Zoom into Ecal
Two electrons
- 2006, Ecal 2 / 3 equipped
     Low energy electrons (1-6 GeV at DESY), high energy electrons (6-50 GeV at CERN)
- 2007, Ecal nearly completely equipped
     High energy pions (6-120 GeV CERN), Tests of embedded electronics
- 2008 FNAL, Ecal completely equipped
      Pions at low energy,
      Data taking with Digital Hcal (>2010?)

---
Exploiting the High Granularity I – Particle Separation
High granularity allows for application of advanced imaging processing techniques
E.g. Hough Transformation
Events recorded in test beam
Two Pions entering
the SiW Ecal
Secondary Muon within
Electron Shower

---
Particle Separation – cont'd
Efficiency of Particle Separation
Separation MIP <-> Electron
1
1
10 MIP Hits
20 MIP Hits
30 MIP Hits
Fraction of common cells
Distance MIP shower axis [mm]
E -> 100% for up to 50% shared hits
Independent of hits generated
by MIP
Full separation for
distances > 2.5 cm
Detection efficiency
Detection efficiency

---
Granularity and Hadronic Cascades
(Start of) Hadronic Showers in the SiW Ecal
Complex and Impressive
Simple but Nice
Scattered Pion
Initial Pion
Interaction
Ejected Nucleon
Outgoing
Fragments
Inelastic Reaction in SiW Ecal
Nucleon Ejection in SiW Ecal
High granularity permits detailed view into hadronic shower

---
Elastic Scattering

---
Types of interactions of hadrons
Modern Bubble Chamber
π 2 GeV
π 8 GeV
- Classification of hadronic interactions
- Large potential for application of pattern recognition algorithms
   or learning algorithms
   Basic Question: “How many particles are in the calorimeter”

---
Hadronic models in GEANT4
Variety of models available to describe hadronic showers
Discriminative power by high granularity !?
“Series of thin targets” (See A. Dotti's talk on G4)

---
Finding the Interaction in the SiW Ecal
        Correlation:
True Interaction <-> Found Interaction
Distribution of found interaction layers
  Determination precise to two layers
    (Overall Layer thickness ~7mm max.)
Good agreement between Data
and Simulation (G4, here QGSP_BERT)
Granularity allow for resolving interaction layer with high resolution
High energy cross sections well implemented in G4 simulation

---
Transversal Shower Profiles and Shower Radius
Affects overlap of showers <-> Importance for PFA
Data compared
with QGSP_BERT
Data compared
with QGSP_BERT
Transverse
Profiles
Rhit/mm
Rhit/mm
Shower
Radius
Ebeam/GeV
Small Energy ok for 'BERT' models
Towards high energy: Underestimation of Content in SiW Ecal
Relatively small difference between models (~15%)
<Rhit>/mm

---
Longitudinal Energy Profiles
Sensitivity to different shower components
Shower Components:
- electrons/positrons
  knock-on, ionisation, etc.
- protons
  from nuclear fragmentation
- mesons
- others
- sum
Depth
Significant Difference between Models
- Particularly for short range component
  (protons)
Granularity of SiW Ecal allows
(some) disentangling of components
Further studies for shower decomposition
are ongoing
Depth
<E>/MIPS
<E>/MIPS

---
Energy depositions in different calorimeter depths
Layer 1-3:
Nuclear breakup
Layer 5-20:
elm. component
Layer 30-50:
Shower hadrons

---
Summary and Outlook
- Successful R&D for a highly granular electromagnetic calorimeter
- Detector concept is built on Particle Flow
   Physics Prototype (2005-2009):
    - Energy resolution ~17%/√E
     - Signal to Noise Ratio ~8/1
     - Stable calibration
   Technological Prototype (2010-...):
     - Mechanical concept validated with demonstrator
     - Silicon Wafer technology at hand
     - Front End Electronics will be challenging
       Embedded into calorimeter layers, power pulsing
- Capacity of separating particles impressively demonstrated
  by test beam analysis
- Unprecedented realistic views into hadronic showers
  thanks to high granularity
  'Modern bubble chamber'
- Coping with vast amount of information is challenging
  The harvest is just starting

---
Backup Slides

---
Jet Energy Resolution
Final state contains high energetic jets from e.g. Z,W decays
Need to reconstruct the jet energy to the utmost precision !
Jet energy carried by …
- Charged particles (e±, h±,μ±)): ‏65%
   Most precise measurement by Tracker
   Up to 100 GeV
- Photons: 25%
  Measurement by Electromagnetic
   Calorimeter (ECAL)
- Neutral Hadrons: 10%
  Measurement by Hadronic
  Calorimeter (HCAL) and ECAL
%sigma_{Jet}=sqrt{%sigma^2_{Track}+%sigma^2_{Had.}+%sigma^2_{elm.}+%sigma^2_{Confusion}}
Tracker Momentum Resolution GeV/c

---
Confusion Term
- Base measurement as much as possible on measurement of charged particles
   in tracking devices
 - Separate of signals by charged and neutral particles in calorimeter
- Complicated topology
  by (hadronic) showers
- Correct assignment
  of energy nearly impossible
⇒ Confusion Term
Need to minimize the confusion
term as much as possible !!!

---
Detector and Calorimeter Concept – Particle Flow
Jet energy measurement by measurement of individual particles
    Maximal exploitation of precise tracking measurement
large radius and length
  - to separate the particles
large magnetic field
  - to sweep out charged tracks
“no” material in front of calorimeters
  - stay inside coil
small Molière radius of calorimeters
  - to minimize shower overlap
high granularity of calorimeters
  - to separate overlapping showers
Physics Goals at the ILC demand the
Construction of Highly Granular Calorimeters!!!
Emphasis on tracking capabilities of calorimeters