   Status of Ecal(s) for ILD
        Roman Pöschl
        LAL Orsay
ILD Meeting at LCWS11 at Granada Sept. 2011

---
Subdetector components IV - Electromagnetic calorimeter
Basic Requirements
The SiW Ecal in the ILD Detector
- Extreme high granularity
- Compact and hermetic
Basic Choices
- Tungsten as absorber material
   - X0=3.5mm, RM=9mm. λI=96mm
   - Narrow showers
   - Assures compact design
- Silicon as active material
        or
- Scintillator as active material
Ecal designed as Particle Flow Calorimeter
R&D within CALICE Collaboration

---
Detector Optimisation – Number of Layers/Sensitive Material
Models under study:
1) A pure SiW Ecal Calorimeter with 20 < N < 30 Layers
2) A pure Scintillator Ecal
3) A hybrid solution
    e.g. first 20 layers Si with rear part of calorimeter equipped with
    Scintillator
PFA studies for hybrid calorimeter ongoing
Both options are implemented into Mokka since long
- PFA with silicon well tested already for LOI
- PFA with scintillator is well advancing

---
Technological prototypes
Technological prototype to
address engineering
challenges of detector
Construction
Collaboration between alternative technologies
where possible

---
R&D for Technological Readiness – Detectors
SiW Ecal
Scint Ecal
- Proof of principle with physics prototypes
  Solid backup of full detector simulation by beam test data
- Robustness of calibration over 6 years (at least proven for SiW Ecal)
- Alveolar structures for barrel and end caps
First ASUs expected 2011/12
First ASUs since 2009
First tests in 2011!!!
Progress slowed down
By non-availability of
DAQ2 ←. drop our of
British groups
- Tests of electronics
- Test of power pulsing
   in magnetic field
- Interconnection and
   cooling
→ planned until summer 2012
- Advanced Wafers
  Technology in principle
  at hand but still
  matter of R&D
- Advanced PCBs
  Ultra thin and Ultra flat
- Scintillator strips
  seems to be available
Not clear what can be achieved until time of DBD
All is very much funding driven
Main sources are French in2p3/ANR and new Japanese ILC funding

---
R&D for Technological Readiness – Peripherals
~ 3 cm between Ecal and Hcal
Need to accommodate
- DAQ components
- Power supply components
- Cooling
Issues are addressed and at least we will come up with a list of
open issues and proposals how to address these

---
Embedded electronics - Parasitic effects?
Exposure of front end electronics to electromagnetic showers
Comparison: Beam events
        (Interleaved) Pedestal events
Chips placed in shower maximum
of 70-90 GeV elm. showers
- No sizable influence on noise spectra
  by beam exposure
  ΔMean < 0.01% of MIP ΔRMS < 0.01% of MIP
- No hit above 1 MIP observed
  => Upper Limit on rate of faked MIPs: ~7x10-7
Possible Effects: Transient effects
        Single event upsets

---
Summary of Ecals
- Ecals in s/w baseline
  Both Ecals are well implemented in Mokka
  Solid backup by beam test analyses
- Input for technology part of DBD
All relevant questions are addressed
However, anwers driven by available funding and manpower
- Some points are already achieved:
   - Stable calibration (at least demonstrated for SiW Ecal)
   - No negative impact by embedded electronics
     (goes beyond Ecal matters)
   - Large alveaolar structures are about to be constructed

---
Backup