      Guard ring studies for SiW Ecal of ILD
        Sohail Amjad, Roman Pöschl
        LAL Orsay
CALICE Collaboration Meeting Cambridge/UK Sept. 2012

---
        SiW Ecal - Basics
Basic Requirements
The SiW Ecal in the ILD Detector
- Extreme high granularity
- Compact and hermetic
Basic Choices
- Tungsten as absorber material
   - X0=3.5mm, RM=9mm, I=96mm
   - Narrow showers
   - Assures compact design
- Silicon as active material
  - Support compact design
  - Allows for pixelisation
  - Large signal/noise ratio
SiW Ecal designed as Particle Flow Calorimeter

---
ILD-ECAL

---
Technological Prototype and Silicon Wafer
Si Wafer
4 wafers on one ASU

---
Some details on silicon wafers
- The wafer is surrounded by a guard ring to control the leakage currents.
- Studies conducted 18X18 Cells Wafer (Standard Mokka Implementation).
- Cell size 5mm X 5 mm.
- The typical/default guard Ring size is 1 mm.
- Purpose of the study is to optimize the guard ring size. (Important aspect of wafer design, see Remi's talk)

---
Systematic studies with photons
- The Studies are performed with Single Photons Events at 2 GeV .
- For the single Photon events we test three different sizes to see the effects, 0.001mm ( ~0 ) ,0.5 mm and 1 mm.
- The study concentrates on the effects induced by varying the Guard Ring size.
- A Theta and Phi smearing of initially 10 Degree and later on of 4 Degree was applied to zoom into a particular region.
size 25 bold {Y_Axis}
size 25 bold {X_Axis}

---
The Wafer Map
Interalveolar gap
Interwafer gap
size 25 bold {X_Axis}
size 25 bold {Z_Axis}

---
Hit Loss due to Guard Ring
size 25 bold {N_hits}
size 25 bold {Un Clustered}
size 25 bold {Clustered}
0.001 mm
0.5 mm
1 mm
size 25 bold {Z_Axis}

---
Energy Loss due to Guard Ring
size 25 bold {E_tot}
size 25 bold {Un Clustered}
size 25 bold {Clustered}
0.001 mm
0.5 mm
1 mm
size 25 bold {Z_Axis}

---
Physics Channels
- Two Important channels.
- Six GR sizes in rang 0-8 mm.
- 1 mm standard, for redundancy.
- Mokka 06-07 and ILCSoft 01-10.
- Full detector simulation.

---
Z->uds (Hadronic Z decay at 91GeV )
- ILC will have multijet final states.
- Jets contain photons coming from π°.
- ~60% hadrons start showering in ECAL.
- ECAL resolution utmost important for precise reconstruction of Jets.

---
Comparison of RMS for different sizes
size 20 {{RMS}over{% Sqrt {E _rec}}}
0.001 mm
1 mm
2 mm
3.5 mm
5 mm
8 mm
size 25 {cos {%theta} _jet}

---
Comparison of RMS90 for different sizes
0.001 mm
1 mm
2 mm
3.5 mm
5 mm
8 mm
size 20 {{RMS _{90}}over{% Sqrt {E _rec}}}
size 25 {cos {%theta} _jet}

---
Jet Energy Resolution vs Guard Ring Size
0.001 mm
1 mm
2 mm
3.5 mm
5 mm
8 mm

---
Z->ee Channel (Leptonic Z decay)
- Precisions on Z Mass.
- Calibration of detector.
- Leptons are reconstructed in ECAL.
- Bremsstrahlung photons recovery.
- Higgs via Z recoil Mass.

---
Z Mass reconstruction.

---
Energy Resolution vs Guard Ring Size

---
Conclusions
- Study on Guard ring sizes for single photon events and two standard physics channels at the ILC
- Using standard ILC reconstruction tools it looks as if guard rings of up to 2mm size does not effect the ECAL performance
=> Flexibility of guard ring design
The study has it's importance when defining the layout of the silicon wafers (e.g. when discussing with manufacturers)

---
Effect on Resolution of ECAL
0.001 mm
0.5mm
1mm
size 25 bold {{ %sigma} over { E _ rec} }
size 30 {{{1} over {sqrt(E _rec)} }}

---
Z Mass reconstruction.

---
ILC	- ILD
- International Linear Collider
- e- e+ Collisions
- 500 GeV to 1 TeV.
- Precision.
- ILD (International Large Detector) is one of the two proposed detectors at ILC.