High brightness beam generation with
a photo-cathode 500kV DC gun
Hiroshima University/KEK
Masao KURIKI

---
Contents
- Introduction
- Photo-cathode 500kV DC gun
- HV test and beam test
- Summary

---
Introduction

---
ILC Design parameter

---
ILC electron source (1)
NEA GaAs/GaAsP superlattice cathode.
200kV inverted type DC gun.
>80% pol. , 3.2nC/bunch at IP.

---
ILC electron source (2)
- NEA GaAs/GaAsP for polarization is not compatible to RF Gun; DC photo-cathode gun is the only solution for LC.
- Current density from 200kV gun is limited by space charge resulting ~1ns bunch length.
  - 1ns → 200ps : two SHBs (316.7 and 433.3MHz).
  - 200ps → 20ps : TW 1.3GHz buncher (b=0.75).
  - Solenoid field for focusing.
- It is desirable to increase HV for shorter initial bunch length.
  - Simplfy the bunching section.
  - Potentially less beam loss and less margin.
- Improving 200kV → 500kV, the bunch length becomes 4 times shorter.

---
500kV DC gun

---
HV DC gun program in Japan
- Photo-cathode HV DC gun R&D program has been carried out by a collaboration among JAEA, KEK, Nagoya U. and Hiroshima U. since 2007.
- This is a common effort for multiple projects: ERL light source, Laser Compton Scattering photon source(Quantum Beam project), and Linear Colliders.
- 500kV and high beam current operation has been confirmed in a test beam line.
- The gun is now under commissioning as the injector of Compact ERL at KEK which is a demo-machine for GeV class ERL light source.

---
Impact of HV on emittance
Beam emittance is grown by non-linear space charge.
High field of the gun makes the beam emittace better by preventing the emittace growth.
800pC
80pC
I. V. Bazarov and C. K. Sinclair,
PRSTAB 8, 034202 (2005) .

---
ERL Project in Japan
- The next generation SR light source based on 3 GeV ERL (PERL) has been proposed.
- PERL is extendable to X-ray FEL oscillator.
- For technical demostration, cERL (compact ERL) is now under commissioning.
- cERL: Laser Compton X/γ-ray
  sources.
Parameters	Value
Energy	35/245 MeV
Current	10mA
Emittance (norm.)	0.1-1.0 mm.mrad

---
Quantum Beam Projet
- High brightness X-ray source with LCS (Laser Compton Scatterig) based on Super-conducting accelerator.
- Experimet was carried out at STF (Superconducting Test Facility, KEK) with a L-band NC RF gun.
- A coceptual design with DC PC gun has 400 times more brightness because of the high
  duty.
1.3 GHz L-band
NC RF Gun
Pf=2.0 MW,
E=33MV/m
Optical Cavity
For Laser-Compton
Scattering
Super-Conducting Accelerator
2m x E=20MV/m
Cs2Te photo-cathode
Preparation Chamber

---
500kV DC gun
- 500kV DC biased gun with ceramic insulator.
- High voltage and high field are essential for high brighness and low emittance beam generation.
- Guard rings on the ceramic insulator prevent HV breakdown and ceramic punch through.
- The guard rings are also effective to prenvent cocentration of the bias voltage in a small region.
500kV bias
guard
rings
ceramic
insulator
support
rod
cathode
mount

---
Segmented Struture with guard rings (1)
Segmented
- HV of DC gun has been limited by ceramic insulator destruction.
- The reason is considered to be field emission from the support rod and field concentration by discharge.
- To prevent these phenomena, we employed segmented structure with guard rings.
One insulator
field emitted
electrons
field emitted
electrons

---
Segmented Structure with guard rings (2)
- Guard rings shade the ceramic from electrons emitted from the support rod by field emission.
- The bias voltage is distributed equally among each segments.
- Charge up and voltage concentration resulting ceramic destruction is threfore strongly prevented.
One insulator
Segmented

---
HV and Beam test

---
The 500kV DC gun system
- A 500kV DC photo-cathode gun with a cathode preparation system.
- High pumping ability by IP and NEG for extremely low vacuum pressure, <1e-9 Pa.
- Surface field <10MV/m for less field emission.
|E| (MV/m)
0
10
2
300
400
Z(mm)
500
600
4
6
8

---
JAEA DC gun beam line
- HV and beam test was carried out at JAEADC gun beam line.
- Laser: 5W 532nm.
- sx=0.1mm.
- Water cooled beam
  dump which is cap-
  able to measure the
  beam current.
- Differential pumping
  to prevent cotami-
  nation to the cathode.
steering magnet
500-kV gun
lightbox
beam dump
radiation shield
bending magnet
differential pump
beam profile monitor
beam expander
solenoid

---
500keV Beam Operation
- After HV conditioning up to 550kV, 500kV was quickly achieved.
- > 2.0mA current was achieved with 1.5 W laser and 0.28% QE.
- Vacuum pressure at gun was maintained at UHV during the operation.
0
100
300
500
600
high voltage (kV)
current (mA)
0.0
0.5
1.0
1.5
2.0
2.5
200
400
HV
I
time (minutes)
0
2
6
1e-9
vacuum pressure (Pa)
1e-8
1e-7
1e-6
1e-5
1e-4
1
3
4
5
@gun
@beam dump

---
10mA Beam operation
- 10 mA beam operation has been demonstrated.
- The test was carried out at lower voltage (180keV) due to field emisson from dust which was fixed by wiping.
- 10mA was achieved , but a significant vacuum pressure escalation was observed.
Laser power = 1.6W
QE = 1.5%
HV
0
50
100
150
200
HV (kV)
I (mA)
0
2
4
6
8
10
12
current
time (min.)
0
5
10
15
20
1e-9
Pressure (Pa)
1e-8
1e-7
1e-6
1e-5
0.2e+5
0.4e+5
0.6e+5
0.8e+5
1.0e+5
0.0
radiation
vacuum@gun
vacuum@dump

---
Operational Lifetime
- Operational lifetime was examined by contineous beam operation.
- Beam current decay was observed showing QE degradation.
- Charge lifetime was extracted to be 48C.
- It is enough for LCs, but not sufficient for ERL light source.
Laser power = 0.37W
QE = 0.68%
0.0
0.2
0.4
0.6
0.8
1.0
1.2
current (mA)
HV
I
0
100
300
500
600
high voltage (kV)
200
400
0 10 20 30 40 50 60
time (minutes)
@gun
@beam dump
1e-9
vacuum pressure (Pa)
1e-8
1e-7
1e-6
1e-5
1e-4

---
Move to cERL
- The developed gun has been moved to cERL at KEK.
- Now, the gun is under commissioning.
- The electron beam from the cERL gun has been confirmed.
- Performance of the cERL gun will be examined in the commissioning.
Stay tuned!

---
Summary
- 500kV DC photo-cathode gun is developed for multiple accelerator projects which require highly polarized and/or high brighness electron beam.
- Stable operation at 500kV has been confirmed.
- 10mA beam generation has been demonstrated.
- The gun is now under commissioning for cERL at KEK.
- The technology is applicable for ILC.
  - The bunch length from the gun can be shorten.
  - The bunching section can be simplified.
  - The energy spread could be less.

---
500kV DC gun R&D group
N. Nishimoria), R. Nagaia), S. Matsubaa), R. Hajimaa), M. Yamamotob), Y. Hondab), T. Miyajimab), H. Iijimac), M. Kurikic), M. Kuwaharad)
a) JAEA, b) KEK, c) Hiroshima U., d) Nagoya U.